Garnet feed Calibration

Turn off intensifier

Remove abrasive feed pipe from cutting head

Go to manual cut screen

Position scales under end of tube

Press cut

Time a minute  - check the weight of garnet

Do following calculation

Theoretical value ÷ actual value  ie 350÷500 remember this number

From main screen

Press configure

Enter code  4604

From tabs along bottom select water jet

1st column about 2/3  down

Abrasive 2  calibration

Note current figure (calibration factor)

Multiply figure by the result of the calculation done earlier

Theorectical value ÷ actual value X calibration factor (the smaller the number the slower the wheel turns)

To insert new value

Tap box with value in it

When key pad appears type in value  and enter

Press Done

On next screen press Save & Exit

On main screen press Exit (back to Cylon / Knight Rider screen)

Press to start

The new value will now be read in by the system

Re home machine and you are ready to go